# Text boxes

Drill Points:

LH:  20mm up	10mm fwd (S) 12mm (G)

RH:  As above.  There is a slot in the bolt plate through which the levers can be lifted.  Also not much danger of drilling off the bolt tail if using no more than an 8mm bit.  Stump is attached to the backplate and can be drilled off but it leaves a lot of swarf which can jam the lever cassette.

Lock Information:  Black gloss case with oval cut-out surrounding a silver 5g keyway.  Can be mistaken for Legge.

Levers are mounted on bolt plate and move as a cassette with the bolt.  The silver plate on the front just holds the levers in position and doesn’t lift.

Curtain Pick.

HENDERSON BS