# Text boxes

YALE/LEGGE OLD With SLIDE OFF HARDPLATE

Lock Information:  Dark grey case on the Yale.  Black case on the Legge. 5g keyway, silver curtain, hardplate wraps around keyway extends 2mm below.  Legge type H Levers.

Curtain pick or drill. Legge Decoders will not work as the case is too narrow.

Drill Points:

LH Side:	17mm up (G)    7mm fwd. (S)

RH Side:	17mm up.  NB: Drilling for the stump can shear off the bolt tail.